Till Straumann :: Paul Scherrer Institute
CPSI-CIO EVM Clocking

---
Introduction
These slides explain the clocking scheme for the MRF EVM firmware on the PSI CPSI-CIO platform.

---
Notes for Users of this PPP
Clocking Resources
CLK_A_FPGA_DP_OUT
- Platform features two Si5395 PLLs
- Drive MGT refclks
- Drive event clocks (CLK_x_FPGA_DP_GC)
- Lock A-device to recovered RX clock.
- Use depends on master vs. fanout mode.
B65_L23
Si5395
A
Inp2
CLK_A_FPGA_DP_OUT
B65_L13 GC
Out7
CLK_A_GTH_QSFP0
Out8
Q128 refclk0
CLK_A_GTH_MSH_SFP1
Out9
Q229 refclk0
CLK_B_FPGA_DP_GC
Si5395
B
Out6
B65_L14 GC
Inp2
CLK_B_GTH_MSH
Out7
Q230 refclk0
CLK_B_GTH_QSFP0
Out8
Q128 refclk1
CLK_B_GTH_QSFP1
Out9
Q228 refclk0

---
EVG/Master Mode
CLK_A_FPGA_DP_OUT
- In master mode A-device is unused.
- All MGTs driven by B-device
- Use quad refclk muxes to route refclk from adjacent quads.
B65_L23
Si5395
A
Inp2
CLK_A_FPGA_DP_OUT
B65_L13 GC
Out7
CLK_A_GTH_QSFP0
Out8
Q128 refclk0
CLK_A_GTH_MSH_SFP1
Out9
Q229 refclk0
CLK_B_FPGA_DP_GC
Si5395
B
Out6
B65_L14 GC
Inp2
CLK_B_GTH_MSH
Out7
Q230 refclk0
CLK_B_GTH_QSFP0
Out8
Q128 refclk1
CLK_B_GTH_QSFP1
Out9
Q228 refclk0

---
Fanout Mode
CLK_A_FPGA_DP_OUT
- Both devices used.
- B-device provides
  - MGT refclk for link to master
  - reverse/up TX/event clock (FO→master)
- A-device locked to recovered master clock
- A-device provides downstream TX/event clock (master->FO)
B65_L23
Si5395
A
Inp2
CLK_A_FPGA_DP_OUT
B65_L13 GC
Out7
CLK_A_GTH_QSFP0
Out8
Q128 refclk0
CLK_A_GTH_MSH_SFP1
Out9
Q229 refclk0
CLK_B_FPGA_DP_GC
Si5395
B
Out6
B65_L14 GC
Inp2
CLK_B_GTH_MSH
Out7
Q230 refclk0
CLK_B_GTH_QSFP0
Out8
Q128 refclk1
CLK_B_GTH_QSFP1
Out9
Q228 refclk0

---
EVG vs. Fanout Mode
- Depending on the mode (using recovered clock → fanout mode)
- Firmware uses MGT reference-clock muxes to drive MGT reference clocks:
  - Master mode: all MGTs driven by Si5395_B
  - Fanout mode:
    - Master-directed MGT driven by Si5395_B.
    - Si5395_A locked to recovered master clock.
    - Fanout MGTs driven by Si5395_A.
- Firmware uses mux to drive fanout event clock
  - Master mode: event clock from Si5395_B (CLK_B_FPGA_DP_GC)
  - Fanout mode: event clock from Si5395_A (CLK_A_FPGA_DP_GC)

---
Design Requirements for Your Presentation
EVM Major Clock Domains (Fanout Mode)
Si5395_A
Recovered RX Clock
Event Clk
MGT
MGT
Fanout (one channel shown)
FIFO
RX
TX
Uplink to Master
CPLL
CPLL
FIFO
TX
RX
Up Event Clk
Si5395_B
- event_clk reads RX receiving master stream; can be locked to recovered RX clock.
- up_event_clk generated locally (Si5395_B). Reads + processes RXes from fanout ports; clocks TX to master.
- RXes decoupled with FIFOs (flexible RD clock as long as link not saturated)
- TX and RX of same channel run at slightly different freq.

---
MGT Clocking
- MGTs are internally clocked by CPLLs
  - CPLL operating range 2GHz..6.4GHz
  - CPLL multiplier = 20
  - bit-rate = MGT refclk * 20 * 2 / 4
  - deliberate choice so that CPLL range covers 1Gbps..3Gbps range, i.e., event clocks from 50MHz .. 150MHz.
  - MGT reference clock is twice the event clock rate (CPLL multiplier = 40 is not supported).
  - If needed the range could be increased by switching the RXRATE/TXRATE dividers (hard-connection to 4 ATM).

---
Other Clocking Limitations
- In fanout mode an MMCM is used to phase-shift the regenerated master clock.
- MMCM has a valid operating range from 800MHz..1600MHz.
- Uses a (hardcoded) multiplier of 11 → recovered clock limited to 72.72MHz..145.45MHz!
- The recovered clock is only used in fanout mode (not EVG mode) and it matches the master clock rate:
  - in fanout mode the master event clock is limited to 72.72MHz … 145.45MHz
  - fanout event clock may be decimated and is not affected by this limit.

---
Si5395 Setup in Master Mode
- Set Si5395_B to zero-delay mode operating at suitable frequency (depends on RF reference).
- Make sure event clock is within range 50MHz .. 150MHz.
- Program Out6 to generate event_clock.
- Program Out7, 8 and 9 to generate 2*event_clock.

---
Si5395 Setup in Fanout Mode (No Decimation)
- Set Si5395_B as for master mode (but no RF reference connected; B-device must be free-runnin).
- Make sure master event clock is within range 72.72MHz .. 145.45MHz.
- Set Si5395_A for ZDM mode tracking the master event clock.
- Pick N and R dividers so that
  - Out7..9a use the same N divider
  - Out7 and Out9a use the same R divider value
  - Out8 and Out9 use half the R divider value of Out7 (must still be even). This yields an MGT reference clock that is twice the event clock rate.

---
Si5395 Setup in Fanout Mode With Decimation
- Set Si5395_B and Si5395_A as for normal fanout mode.
- The fanout event clock is now different from the master event clock and must be within the 50MHz..150MHz range.
- Use N and R7,R8,R9 dividers to generate fanout event and MGT clocks
  - if possible use the same N divider as Out9a (ZDM output)
  - program Out7 R divider for fanout event clock (different from Out9a R divider)
  - program Out8, Out9 R dividers to half of Out7 R divider value (must still be even). This yields a fanout MGT reference clock of twice the fanout event rate.

---
Caution When Reprogramming Clocks
- After power-up the Si5395 PLLs have to be initialized *before* loading the firmware image so that stable reference- and event clocks are available.
- Reprogramming the Si5395 PLLs will stop its output clocks for some time. In order to avoid problems with a stopped event clock programming can use this work-around:
  - before programming PLL A switch the EVM to master mode. In this mode PLL-A is unused and reprogramming it causes no problems.
  - before programming PLL B switch the EVM into fanout mode. The event clock is then generated by PLL A and reprogramming PLL-B should not cause problems.
  - Avoid using the so-called 'upstream' embedded EVR (this listens to backwards traffic towards the master). This EVR uses PLL-B for its event clock and could cause problems when accessed while PLL-B is unavailable due to reprogramming.