Till Straumann :: Paul Scherrer Institute
CPSI-CIO EVM Clocking

---
Introduction
These slides explain the clocking scheme for the MRF EVM firmware on the PSI CPSI-CIO platform.

---
Event Clock
 As explained later the MGT reference clock rate must be twice the event clock rate, i.e., the MGT reference clock can not directly be used as the event clock.
In order to maintain a defined phase relationship between the Si5395 reference (regenerated master event clock in the case of the 'A' device or external reference in case of the 'B' device, respectively) and the event clock the latter is generated in the Si5395 PLL rather than dividing the MGT reference (which would introduce an uncontrolled divider phase).
The Si5395 devices should be operated in ZDM mode and the output which generates the event clock must share the same N-divider as the ZDM output. All output R-dividers have to be synchronized. This scheme ensures a defined and reproducible (across power-cycles) phase relationship between the Si5395 reference and the event clock.

---
Notes for Users of this PPP
Clocking Resources
CLK_A_FPGA_DP_OUT
- Platform features two Si5395 PLLs
- Drive MGT refclks
- Drive event clocks (CLK_x_FPGA_DP_GC)
- Lock A-device to recovered RX clock.
- Lock B-device to external reference (from RTM)
- Use depends on master vs. fanout mode.
B65_L23
Si5395
A
Inp2
CLK_A_FPGA_DP_OUT
B65_L13 GC
Out7
CLK_A_GTH_QSFP0
Out8
Q128 refclk0
CLK_A_GTH_MSH_SFP1
Out9
Q229 refclk0
CLK_B_FPGA_DP_GC
Si5395
B
Out6
B65_L14 GC
RTM_IN
Inp2
CLK_B_GTH_MSH
Out7
Q230 refclk0
CLK_B_GTH_QSFP0
Out8
Q128 refclk1
CLK_B_GTH_QSFP1
Out9
Q228 refclk0

---
EVG/Master Mode
CLK_A_FPGA_DP_OUT
- In master mode A-device is unused.
- All MGTs driven by B-device
- Use quad refclk muxes to route refclk from adjacent quads.
- Event clock generated by Out6
- B-device can be locked to external reference (from RTM)
B65_L23
Si5395
A
Inp2
CLK_A_FPGA_DP_OUT
B65_L13 GC
Out7
CLK_A_GTH_QSFP0
Out8
Q128 refclk0
CLK_A_GTH_MSH_SFP1
Out9
Q229 refclk0
CLK_B_FPGA_DP_GC
Si5395
B
Out6
B65_L14 GC
RTM_IN
Inp2
CLK_B_GTH_MSH
Out7
Q230 refclk0
CLK_B_GTH_QSFP0
Out8
Q128 refclk1
CLK_B_GTH_QSFP1
Out9
Q228 refclk0

---
Fanout Mode
CLK_A_FPGA_DP_OUT
- Both devices used.
- B-device provides
  - MGT refclk for link to master
  - reverse/up TX/event clock (FO→master on Out6)
- A-device locked to recovered master clock
- A-device provides downstream TX/event clock (master→FO on Out7)
B65_L23
Si5395
A
Inp2
CLK_A_FPGA_DP_OUT
B65_L13 GC
Out7
CLK_A_GTH_QSFP0
Out8
Q128 refclk0
CLK_A_GTH_MSH_SFP1
Out9
Q229 refclk0
CLK_B_FPGA_DP_GC
Si5395
B
Out6
B65_L14 GC
Inp2
CLK_B_GTH_MSH
Out7
Q230 refclk0
CLK_B_GTH_QSFP0
Out8
Q128 refclk1
CLK_B_GTH_QSFP1
Out9
Q228 refclk0

---
EVG vs. Fanout Mode
- Depending on the reference clock mode (RFSEL modes 5+7 in the 'ClockControl' register which refer to 'recovered clock' do enable fanout mode)
- Firmware uses MGT reference-clock muxes to drive MGT reference clocks:
  - Master mode: all MGTs driven by Si5395_B
  - Fanout mode:
    - Master-directed MGT driven by Si5395_B.
    - Si5395_A locked to recovered master clock.
    - Fanout MGTs driven by Si5395_A.
- Firmware uses mux to drive fanout event clock
  - Master mode: event clock from Si5395_B (CLK_B_FPGA_DP_GC)
  - Fanout mode: event clock from Si5395_A (CLK_A_FPGA_DP_GC)

---
Design Requirements for Your Presentation
EVM Major Clock Domains (Fanout Mode)
Si5395_A
Recovered RX Clock
Event Clk
MGT
MGT
Fanout (one channel shown)
FIFO
RX
TX
Uplink to Master
CPLL
CPLL
FIFO
TX
RX
Up Event Clk
Si5395_B
- event_clk reads RX receiving master stream; can be locked to recovered RX clock.
- up_event_clk generated locally (Si5395_B). Reads + processes RXes from fanout ports; clocks TX to master.
- RXes decoupled with FIFOs (flexible RD clock as long as link not saturated)
- TX and RX of same channel run at slightly different freq.

---
MGT Clocking
- MGTs are internally clocked by CPLLs
  - CPLL operating range 2GHz..6.4GHz
  - CPLL multiplier = 20
  - bit-rate = MGT refclk * 20 * 2 / 4
  - deliberate choice so that CPLL range covers 1Gbps..3Gbps range, i.e., event clocks from 50MHz .. 150MHz.
  - MGT reference clock is twice the event clock rate (CPLL multiplier = 40 is not supported).
  - If needed the range could be increased by switching the RXRATE/TXRATE dividers (hard-connection to 4 ATM).

---
Other Clocking Limitations
- In fanout mode an MMCM is used to phase-shift the regenerated master clock.
- MMCM has a valid operating range from 800MHz..1600MHz.
- Uses a (hardcoded) multiplier of 11 → recovered clock limited to 72.72MHz..145.45MHz!
- The recovered clock is only used in fanout mode (not EVG mode) and it matches the master clock rate:
  - in fanout mode the master event clock is limited to 72.72MHz … 145.45MHz
  - fanout event clock may be decimated and is not affected by this limit.

---
Si5395 Setup in Master Mode
- Set Si5395_B to zero-delay mode operating at suitable frequency (depends on RF reference).
- Make sure event clock is within range 50MHz .. 150MHz.
- Program Out6 to generate event_clock. Make sure to share N divider with ZDM output.
- Program Out7, 8 and 9 to generate 2*event_clock (MGT reference clock).
- SI5395_B may lock to external reference or operate in free-running mode (automatically enters this mode when there is no reference detected).

---
Si5395 Setup in Fanout Mode (No Decimation)
- Set Si5395_B as for master mode (but no RF reference connected; B-device must be free-runnin).
- Make sure master event clock is within range 72.72MHz .. 145.45MHz.
- Set Si5395_A for ZDM mode tracking the master event clock.
- Pick N and R dividers so that
  - Out7..9a use the same N divider
  - Out7 and Out9a use the same R divider value
  - Out8 and Out9 use half the R divider value of Out7 (must still be even). This yields an MGT reference clock that is twice the event clock rate.

---
Si5395 Setup in Fanout Mode With Decimation
- Set Si5395_B and Si5395_A as for normal fanout mode.
- The fanout event clock is now different from the master event clock and must be within the 50MHz..150MHz range.
- Use N and R7,R8,R9 dividers to generate fanout event and MGT clocks
  - if possible use the same N divider as Out9a (ZDM output)
  - program Out7 R divider for fanout event clock (different from Out9a R divider)
  - program Out8, Out9 R dividers to half of Out7 R divider value (must still be even). This yields a fanout MGT reference clock of twice the fanout event rate.

---
Caution When Reprogramming Clocks
- After power-up the Si5395 PLLs have to be initialized *before* loading the firmware image so that stable reference- and event clocks are available.
- Reprogramming the Si5395 PLLs will stop its output clocks for some time. In order to avoid problems with a stopped event clock programming can use this work-around:
  - before programming PLL A switch the EVM to master mode. In this mode PLL-A is unused and reprogramming it causes no problems.
  - before programming PLL B switch the EVM into fanout mode. The event clock is then generated by PLL A and reprogramming PLL-B should not cause problems.
  - Avoid using the so-called 'upstream' embedded EVR (this listens to backwards traffic towards the master). This EVR uses PLL-B for its event clock and could cause problems when accessed while PLL-B is unavailable due to reprogramming.